# The Package Multis

Installation

TMultiPanel

TMultiButton

TMultiButtonStylemanager

TMultiplexSlider

TMultiSeperator

## Installation
The package is located in the following Github account: https://github.com/wennerer/Multis
After the package has been cloned or downloaded, it can be installed in Lazarus. To do this, open Lazarus and click on Open Package File (.lpk)... under Package.

Now navigate to the Multis folder and select the file multis.lpk.

The following window will open:

Click on Use and then Install.

Confirm this dialogue with Yes:

Now there is a new Multi tab in the palette selection.

## TMultiPanel
### Properties
Action	: The Action associated with the control
Align	: Specifies the placement of the control inside its Parent.
Anchors	: The set of anchor definitions for this control
Autosize	: Allows automatic adjustment of the size for the control, according to its content
BidiMode	: Customization (of text controls) in bidirectional reading environments
BorderSettings	: The properties of the border
BorderSettings.Between	: The space between inner- and outerborder
BorderSettings.InnerColor	: The color of the innerborder
BorderSettings.InnerWidth	: The width of the innerborder
BorderSettings.OuterColor	: The color of the outerborder
BorderSettings.OuterWidth	: The width of the outerborder
BorderSpacing	: Determines the inner and outer border spacing for this control
Caption	: The text that the user writes in the panel
CaptionAlignment	: Alignment of the text in the caption (left, center, right)
CaptionHorMargin	: The horizontal distance of the text in the text rectangle (only effective with	taLeftJustify)
CaptionLayout	: Alignment of the text in the caption (top, center, bottom)
CaptionVerMargin	: The vertical distance of the text in the text rectangle (only effective with tlTop)
CaptionWordbreak	: Allows a line break in the caption
ColorEnd	: The end color of the panel ( for color gradient)
ColorGradient	: The direction of the gradient
ColorStart	: The start color of the panel ( for color gradient)
Constraints	: The minimum and maximum Width and Height for the control
Cursor	: The shape of the mouse pointer, when the mouse is over this control
DoubleBuffered	: Allows to reduce flicker in the painting of the control
DragCursor	: The cursor shape shown while the control is dragged
DragKind	: The operation when the control is dragged - Drag or Dock
DragMode	: Allows the user to drag the control
DrawACustomPanel	: Opens an editor where you can draw a panel
DropDownMenu	: The properties of the dropdownmenu
DropDownMenu.Active	: Activates the dropdown function
DropDownMenu.Compressed	: Properties of the compressed panel
DropDownMenu.Compressed.Active : Makes the selection the starting value
DropDownMenu.Compressed.Height : The height of the compressed panel
DropDownMenu.Compressed.Width : The width of the compressed panel
DropDownMenu.Direction	: The fold-out direction
DropDownMenu.Hotspot	: Defines the area in which a click is effective, only active with	DropDownMenu.Active and trPinned (only at runtime!)
DropDownMenu.Speed	: The drawing speed (timer intervall)
DropDownMenu.Step	: The drawing steps (pixels)
DropDownMenu.Stretched	: Properties of the streched Panel
DropDownMenu.Stretched.Active	: Makes the selection the starting value
DropDownMenu.Stretched.Height	: The height of the stretched panel
DropDownMenu.Stretched.Width.	: The width of the stretched panel
DropDownMenu.Trigger	: Trigger
Font	: The font to be used for text display in this panel
Height	: The vertical size of the control
HelpContext	: The ID for context-sensitive Help on this control
HelpKeyword	: The keyword for context-sensitive Help on this control
HelpType	: Determines whether context-sensitive Help is selected by numeric ID or	keyword
Hint	: The text to show in the Hint window for the control
ImageIndex	: The Index of a Image in a ImageList
ImageLeft	: The coordinate of the left edge of a Image
Images	: A list for including images
ImageTop	: The coordinate of the top edge of a Image
ImageWidth	: The unique width of all images in the list
Left	: The client coordinate of the left edge of the control
RndRctRadius	: Corner diameter if the geometric shape is RoundRect
Style	: The geometric shape of the panel
Top	: The client coordinate of the top edge of the control
Visible	: Allows to show or hide the control, and all of its children
Width	: The horizontal extent of the control
Appear	: makes the panel appear (only at runtime!)
Disappear	: makes the panel disappear (only at runtime!)
AnimationSpeed	: Speed for Appear bzw. Disappear (default 0,05) (only at runtime!)
ParentAsBkgrd	: Background of the panel takes on the colour of the parent (only at runtime!)

### Events
OnChangeBounds	: Event handler for a change of the Bounds of the control

OnClick	: Notification handler for mouse clicks

OnCompressed	: Handler when the panel is compressed, only active when	DropDownMenu.Active

OnDragDrop	: This handler determines the action on an drop onto this control, in a drag-drop	operation
OnDragOver	: Event handler for a control being dragged over this control
OnEndDrag	: Notification handler for the end of a dragging operation
OnEnter	: Handler for control receiving the focus

OnExit	: Handler for control loosing the focus; This is a good place for checking the	finished user input

OnKeyDown	: Handler for keyboard key pressed

OnKeyPress	: Handler for a character entered by the user

OnKeyUp	: Handler for keyboard key released

OnMouseDown	: Event handler for mouse button going down

OnMouseEnter	: Event handler for mouse entering the area of the control

OnMouseLeave	: Event handler for mouse leaving the area of the control

OnMouseMove	: Event handler for mouse movement within the control

OnMouseUp	: Event handler for mouse button going up

OnStartDrag	: Event handler for the start of a dragging operation
OnStreched	: Handler wenn das Panel ausgeklappt ist, nur aktive wenn	DropDownMenu.Active

### Public procedures

procedure MouseMove({%H-}Shift: TShiftState; X, Y: Integer);override;
procedure MouseDown({%H-}Button: TMouseButton;{%H-}Shift: TShiftState; X, Y: Integer);override;
procedure MouseUp({%H-}Button: TMouseButton; {%H-}Shift: TShiftState; {%H-}X, {%H-}Y: Integer);override;
procedure LoadFromFile(aFileName: string);
procedure InvalidateBackground;
procedure ParentInputHandler({%H-}Sender: TObject; Msg: Cardinal);
procedure Notification(AComponent: TComponent;Operation: TOperation); override;
constructor Create(AOwner: TComponent); override;
destructor Destroy; override;
procedure MouseEnter; override;
procedure MouseLeave; override;
procedure Paint; override;
### Description

You will find the MultiPanel in the Multis tab.

The shape of the MultiPanel can be influenced with the Style property.
mpsRect:	mpsEllipse:	mpsRoundRect:
 The corner radius can be set	with RndRctRadius .	Default setting is 40
mpsCustom:
By default, mpsCustom has a triangle behind it. To draw a custom panel, click on the 3 dots	behind DrawACustomPanel .

A property editor will open:
If you now click on New, you can simply draw	the shape of the MultiPanel with the mouse.If	you click on Use, the MultiPanel shape is	adopted. With Discard the MultiPanel shape is	not accepted and the editor is closed. With Save	you can save a drawn shape and with Load you	can get it again. Grid displays an auxiliary grid	that may help you when drawing.
Remember it must be set to	mpsCustom!

At runtime, MultiPanels saved in advance can also be loaded with LoadFromFile.

To change the colour of the MultiPanel you need the properties ColorStart, ColorEnd and ColorGradient. To get a single-coloured MultiPanel, ColorStart and ColorEnd must be the same. Otherwise, the composition of the three properties determines the appearance.
gcSpread:	gcRadiant:	gcAlternate:

Alternately sets one pixel	each to Start- and	EndColor.

gcHorizontal:	gcVertical:

If you want to highlight the border, you can use the properties of the BorderSettings.
To create a border, simply select a colour. If you	do not want a border, use clNone.

BorderSettings.Between	: The space between inner- and outerborder
BorderSettings.InnerColor	: The color of the innerborder
BorderSettings.InnerWidth	: The width of the innerborder
BorderSettings.OuterColor	: The color of the outerborder
BorderSettings.OuterWidth	: The width of the outerborder

The Appear, Disappear and AnimationSpeed properties can only be set at runtime!
To make an invisible MultiPanel appear, use the property Appear.
Example code:
procedure TForm1.MultiButton1Click(Sender: TObject);
begin
 MultiPanel1.Appear:= true;
end;

To make a visible MultiPanel disappear, use the property Disappear.
Example code:
procedure TForm1.MultiButton2Click(Sender: TObject);
begin
 MultiPanel1.Disappear:= true;
end;
With the property AnimationSpeed the speed of appearance or disappearance can be influenced.
The default value is 0.05. The smaller the value, the slower the animation. With a value of 0.001 it is already very slow.
Example code:
MultiPanel1.AnimationSpeed:= 0.001;

If you select something other than mpsRect as the geometric shape (Style property), a part of the background of the MultiPanel becomes visible. These visible corners take on the colour set in the parent. If there are self-drawn lines in the parent, for example, these are also shown. This happens because the property ParentAsBkgrd is set to true by default.
ParentAsBkgrd := true	ParentAsBkgrd := false

This setting makes sense especially when the	parent changes its size. Because then, for	example, the drawn line is not scaled correctly	here.

If the parent has a colour gradient, it is possible to compensate for the scaling problem by calling the procedure InvalidateBackground.
Example code:
procedure TForm1.FormChangeBounds(Sender: TObject);
begin
 MultiPanel1.InvalidateBackground;
end;

To create a DropDown menu (hamburger menu), first set the property DropDownMenu.Active to true.
The MultiPanel now shows the compressed state. The positioning can be done	with the mouse or the properties Left or Top (of course anchors can also be set).	The size can simply be dragged with the mouse or assigned with the properties	DropDownMenu.Compressed.Height or	DropDownMenu.Compressed.Width. If the size fits, switch to the expanded state	with the properties DropDownMenu.Stretched.Active or	DropDownMenu.Compressed.Active. Now the desired size can also be set by	dragging with the mouse or with the properties	DropDownMenu.Stretched.Height or DropDownMenu.Stretched.Width. It is recommended to place the desired child controls (buttons etc.) in this state. The direction in which the MultiPanel unfolds is determined by the property DropDownMenu.Direction.	The following options are available:	TDirection = (LeftTop_RightBottom,RightTop_LeftBottom,LeftBottom_RightTop,RightBottom_LeftTop)
The speed of the unfolding can be influenced by the properties DropDownMenu.Speed and DropDownMenu.Step . The timer interval with which the unfolding is called is hidden behind Speed. To slow down, increase this value to the desired speed. With Step you can set the number of additional pixels that are drawn per interval. If you want to unfold faster, increase the value for Step.
With DropDownMenu.Trigger you determine the trigger for the unfolding.	The following possibilities are available:	TTrigger = (trClick,trHover,trPinned)	With trClick you have to click in the panel, with trHover it is enough to move the mouse over it. With trPinned, you must click in the MultiPanel, but it only collapses if you click in a definable hotspot (DropDownMenu.Hotspot).

## TMultiButton
### Properties
Action	: The Action associated with the control
Align	: Specifies the placement of the control inside its Parent
AllowsUp	: Allows a pressed button to be set to not pressed
Anchors	: The set of anchor definitions for this control
AutoSize	: Allows automatic adjustment of the size for the control, according to its content
BidiMode	: Customization (of text controls) in bidirectional reading environments
BorderColor	: The color of the border
BorderSpacing	: Determines the inner and outer border spacing for this control
BorderWidth	: The whidth of the border
Caption	: The text that the user writes in the button
CaptionAlignment	: Alignment of the text in the caption (left, center, right)
CaptionHorMargin	: The horizontal distance of the text in the text rectangle (only effective with	taLeftJustify)
CaptionLayout	: Alignment of the text in the caption (top, center, bottom)
CaptionVerMargin	: The vertical distance of the text in the text rectangle (only effective with tlTop)
CaptionWordbreak	: Allows a line break in the caption
ColorEnd	: The end color of the button ( for color gradient)
ColorGradient	: The direction of the gradient
ColorStart	: The start color of the button ( for color gradient)
Constraints	: The minimum and maximum Width and Height for the control
DisabledAlphaBValue	:
DisabledColor	:
Down	: The Button has been set in the Down state
DragCursor	: The cursor shape shown while the control is dragged
DragKind	: The operation when the control is dragged - Drag or Dock
DragMode	: Allows the user to drag the control
Enabled	: Determines whether the control reacts on mouse or keyboard input
FocusAlphaBValue	: How translucent the focusframe is (0=transparent, 255=opaque)
FocusColor	: The color of the Fokusframe/Foregroundfocus when the Control has the focus
FocusFrameOn	: Indicates when the button has focus
FocusFrameWidth	: The whidth of the focus-frame
Font	: The font to be used for text display in this button
ForegroundFocusOn	: Indicates when the button has focus
GroupIndex	: The Index within the group of MultiButtons
Height	: The vertical size of the control.The height of the MultiButton is minus	HoverFrameWidth
HelpContext	: The ID for context-sensitive Help on this control
HelpKeyword	: The keyword for context-sensitive Help on this control
HelpType	: Determines whether context-sensitive Help is selected by numeric ID or	keyword
Hint	: The text to show in the Hint window for the control
HoverEndColor	: The endcolor of a hoverevent
HoverFontColor	: The color of the Caption during one hoverevent
HoverImageIndex	: The Index of a Image in a ImageList when during one hoverevent
HoverOn	: Allows to show or hide a hoverevent
HoverStartColor	: The startcolor of a hoverevent
ImageIndex	: The Index of a Image in a ImageList
ImageLeft	: The coordinate of the left edge of a Image
Images	: A list for including images
ImageTop	: The coordinate of the top edge of a Image
ImageWidth	: The unique width of all images in the list
Left	: The client coordinate of the left edge of the control
MessageButton	: A message button to display information or to provide a second integrated	button
MessageButton.Alignment	: The position of the messagebutton
MessageButton.BorderColor	: The color of the border
MessageButton.BorderWidth	: The whidth of the border
MessageButton.CalculateAlthoughInvisible : Is required if the MessagButton is only visible at runtime
MessageButton.Caption	: The text that the user writes in the messagebutton
MessageButton.CaptionAlignment	: Alignment of the text in the caption (left, center, right)
MessageButton.CaptionHorMargin	: The horizontal distance of the text in the text rectangle (only effective with	taLeftJustify)
MessageButton.CaptionLayout	: Alignment of the text in the caption (top, center, bottom)
MessageButton.CaptionVerMargin	: The vertical distance of the text in the text rectangle (only effective with tlTop)
MessageButton.ColorEnd	: The end color of the messagebutton ( for color gradient)
MessageButton.ColorGradient	: The direction of the gradient
MessageButton.ColorStart	: The start color of the messagebutton ( for color gradient)
MessageButton.Font	: The font to be used for text display in this button
MessageButton.Height	: The vertical size of the control
MessageButton.HoverColor	: The color of a hoverevent
MessageButton.HoverOn	: Allows to show or hide a hoverevent
MessageButton.ImageIndex	: The Index of a Image in a ImageList
MessageButton.ImageLeft	: The coordinate of the left edge of a Image
MessageButton.Images	: A list for including images
MessageButton.ImageTop	: The coordinate of the top edge of a Image
MessageButton.ImageWidth	: The unique width of all images in the list
MessageButton.PositionFactor	: Position factor, only active if alSE,alSW,alNW,alNE,alW,alE,alN,	alS,alRightIn,alLeftIn,alTopIn,alBottomIn
MessageButton.PresdColBlendVal	: How translucent the pressedcolor is (0=transparent, 255=opaque)
MessageButton.PressedColor	: The color of the messagebutton when it is pressed
MessageButton.ShowBorder	: Allows to show or hide a border
MessageButton.ShowPressed	: Allows to show or hide the pressedoption
MessageButton.Style	: The geometric shape of the messagebutton
MessageButton.Visible	: Allows to show or hide the control, and all of its children
MessageButton.Width	: The horizontal extent of the control
MultiButton_StyleManager	: Simplifies the design of the MultiButton
PopupMenu	: A context-sensitive menu that pops up when the right mouse button is clicked	over this control
PressedEndColor	: The end color of the button when it is pressed (for color gradient)
PressedFontColor	: The color of the text of the caption when the button is pressed
PressedImageIndex	: The Index of a Image in a ImageList when the Button is pressed
PressedStartColor	: The starting color of the button when it is pressed (for color gradient)
RndRctRadius	: Corner diameter if the geometric shape is RoundRect
ShowBorder	: Allows to show or hide a border
ShowHint	: When True, the Hint text is shown when the mouse hovers over the control
ShowMsgButtonInGroup	: Shows the message button on the MultiButton in a group
Style	: The geometric shape of the button
TabOrder	: Determines the sequence of control navigation when the user presses the Tab	key
TabStop	: Allows the user to navigate to this control, by pressing the Tab key
Top	: The client coordinate of the top edge of the control
Visible	: Allows to show or hide the control, and all of its children
Width	: The horizontal size of the control.The width of the MultiButton is minus	HoverFrameWidth

### Events
OnClick	: Notification handler for mouse clicks

OnDragDrop	: This handler determines the action on an drop onto this control, in a drag-drop	operation
OnDragOver	: Event handler for a control being dragged over this control
OnEndDrag	: Notification handler for the end of a dragging operation
OnEnter	: Handler for control receiving the focus

OnExit	: Handler for control loosing the focus; This is a good place for checking the	finished user input

OnKeyDown	: Handler for keyboard key pressed

OnKeyPress	: Handler for a character entered by the user

OnKeyUp	: Handler for keyboard key released

OnMouseDown	: Event handler for mouse button going down

OnMouseEnter	: Event handler for mouse entering the area of the control

OnMouseLeave	: Event handler for mouse leaving the area of the control

OnMouseMove	: Event handler for mouse movement within the control

OnMouseUp	: Event handler for mouse button going up

OnStartDrag	: Event handler for the start of a dragging operation
MessageButton.OnClick	: Notification handler for mouse clicks
MessageButton.OnMouseMove	: Event handler for mouse movement within the control

### Description